MULTI PURPOSE MACRO PRE-PROCESSOR
Documentation (Part - 1)

Submitted By:
Uditi Arora
(2016UCP1415)

Introduction
The pre-processor has been designed for Assembly Language (NASM/GAS). This pre-processor allows the users to define macros with any number of parameters,the format for which has been covered in detail in this document . The preproceesor reads from a .asm file and writes the whole code again after expansion into a new file.

The basic purpose of designing this macro processor is to make the work of the programmer easier by reducing the work of copying/writing the same statements with different variables again. It’s functions essentially involve substitution of one group of characters or lines for another.

The design of this pre-processor is not directly related to the architecture of the computer on which it is to run.
This model supports nested macros (number of levels depend on the stack mantaining function calls) as well but use of lables is not allowed because of implementation problems. One of the features of this pre – processor is that it does not dispaly comments everytime a macro is called.

The final file does not include the defined macro because invocated macros have already been expanded and the orignal macros are no longer needed.

Defining a Macro

The keyword used here in order to define a macro is “#DEF”. Every macro to be declared starts with this and ends with the keyword “END” . The arguments are declared one in each line. The name of the macro follows the rules of C – style variable naming.
These can be declared in the following syntax:
#DEF macro_name
&arg1
&arg2
.
.
.
&argN

macro body(code	)
.
.
.
.

END

Some Important points to be taken care of:
1. & can only be used as a prefix for parameters and not for variables.
2. Only one parameter can be written in one line.
3. Leave a line after END statement(preferably).

Invocation of a Macro
The invocation format is a bit different from the definition format . In this the parameters can be passed in one line separated by commas.
The following illustrates this:
macro_name arg1,arg2,...,argN

Comments in Macro Definitions
A comment starts with // in the defintion of macro.
It does not appear in the expanded code.

Features Covered:
1. No restriction on number of arguments.
2. Nested Macros supported.
3. Proper replacement of arguments without disturbing the indentation of the code.
4. Comments are removed before expansion.

Some Examples Are:

The following code calculates the largest of three numbers.
In this macro has been used to print

The code is :

#DEF macro_to_print
&msg1
&len1
mov eax,4
mov ebx,1	// commments
mov ecx,&msg1
mov edx,&len1
int 80h
END

section .data
numb1 dd '80'
numb2 dd '99'
numb3 dd '90'
msg1: db "the greatest number is:"
len1 equ $-msg1

section .bss
lrgst resb 2
section .text
global _start
_start:
mov ecx,[numb1]
cmp ecx,[numb2]
jg thirdnum
mov ecx,[numb2]

thirdnum:
cmp ecx,[numb3]
jg _exit
mov ecx,[numb3]
_exit:
mov [lrgst],ecx
macro_to_print msg1,len1

macro_to_print lrgst,2

mov eax,1
mov ebx,0
int 80h

Output of the pre-processor:

section .data
numb1 dd '80'
numb2 dd '99'
numb3 dd '90'
msg1: db "the greatest number is:"
len1 equ $-msg1

section .bss
lrgst resb 2
section .text
global _start
_start:
mov ecx,[numb1]
cmp ecx,[numb2]
jg thirdnum
mov ecx,[numb2]

thirdnum:
cmp ecx,[numb3]
jg _exit
mov ecx,[numb3]
_exit:
mov [lrgst],ecx
mov eax,4
mov ebx,1
mov ecx,msg1
mov edx,len1
int 80h

mov eax,4
mov ebx,1
mov ecx,lrgst
mov edx,2
int 80h

mov eax,1
mov ebx,0
int 80h

Same example can be run using nested macro :

#DEF macro_to_print
&msg1
&len1
mov eax,4
mov ebx,1	// comments
mov ecx,&msg1	// comments

#DEF nested_macro
&len1

mov edx,&len1	// nested macro
END
int 80h
END

section .data
numb1 dd '80'
numb2 dd '99'
numb3 dd '90'
msg1: db "the greatest number is:"
len1 equ $-msg1

section .bss
lrgst resb 2
section .text
global _start
_start:
mov ecx,[numb1]
cmp ecx,[numb2]
jg thirdnum
mov ecx,[numb2]

thirdnum:
cmp ecx,[numb3]
jg _exit
mov ecx,[numb3]
_exit:
mov [lrgst],ecx
macro_to_print msg1,len1

macro_to_print lrgst,2

mov eax,1
mov ebx,0
int 80h

The result is:

section .data
numb1 dd '80'
numb2 dd '99'
numb3 dd '90'
msg1: db "the greatest number is:"
len1 equ $-msg1

section .bss
lrgst resb 2
section .text
global _start
_start:
mov ecx,[numb1]
cmp ecx,[numb2]
jg thirdnum
mov ecx,[numb2]

thirdnum:
cmp ecx,[numb3]
jg _exit
mov ecx,[numb3]
_exit:
mov [lrgst],ecx
mov eax,4
mov ebx,1
mov ecx,msg1

mov edx,len1
int 80h

mov eax,4
mov ebx,1
mov ecx,lrgst

mov edx,2
int 80h

mov eax,1
mov ebx,0
int 80h